## 6.6	Voice Setup Success Rate (VSSR)

### 6.6.1	Description and Title

Voice Setup Success Rate measures the succeeded voice call connections after call attempts initiated by user. Success is defined differently based on the measurement point.

Depending on the application of VSSR measurement, voice setup success can have different definitions. Two options are provided in this document:

Option A: When MO side successfully received the feedback from MT side (Ringing, call answered, etc.), the call attempt is considered to be successful. This definition focuses on the perception of end user.

Option B: When the bearer service of MO / MT side is successfully setup, the MO / MT call attempt is considered to be successful. This definition focuses on the network resource availability.

VSSR option A and option B are different KPIs, have different meanings and different values. In this document, they are referred by different notations: VSSR (Option A) and VSSR (Option B).

### 6.6.2	Purpose

### Voice Setup Success Rate measures the accessibility of voice calls which includes mobile originated and mobile terminated CS (circuit-switched) for 2G and/or 3G and VoLTE for 4G.  This rate is for ALL voice calls, and includes mobile originated and terminated calls. The purpose is to compare success rate measurements by at least one element on a daily basis accumulated monthly.

### 6.6.3	Applicable Product Categories

The measurement applies to product category 9.2 as defined in the Measurement Applicability Table (Normalization Units), Appendix A, Table A-2.

### 6.6.4	Detailed Description

- Terminology

          - AMR: Adaptive Multi Rate

          - CN: Core Network

          - CS: Circuit Switched

          - eNB: eNodeB

          - IMS: IP Multimedia Subsystem

          - KPI: Key Performance Index

          - MME: Mobility Management Entity

          - MO: Mobile Originate

          - MSC: Mobile Switching Centre

          - MT: Mobile Terminate

          - Op: Option

          - P-CSCF: Proxy-Call Session Control Function

          - RAB: Radio Access Bearer

          - RANAP: Radio Access Network Application Part

          - RNC: Radio Network Controller

          - RRC: Radio Resource Control

          - SIP: Session Initiation Protocol

          - SSR: Setup Success Rate

          - TCATT: # of Total Call ATTempts

          - TSFAL: # of Total Setup FAiLed calls

          - TSSUC: # of Total Setup SUCceeded calls

          - UE: User Equipment

          - VoLTE: Voice over LTE

          - VSSR: Voice Setup Success Rate

          - 4G-SIP-VSSR:  Voice Setup Success Rate formula for all SIP invites and first responses then becomes: (C1+C2) / C3 (when counted for all INVITE transactions ends up as a network end-to-end measure as measured by UE, P-CSCF or Network Probe)

- Counting Rules

- C1:  First 180 Ringing or 200 OK whichever comes first corresponding with INVITE dialog is considered success. Note: Multiple 180s on same call should not be counted, e.g. multiple 180s due to missing PRACK.

- C2:  4xx/5xx/6xx from list below received without prior provisional response for INVITE is also considered success

            - 400 Bad Request

            - 404 Not Found

            - 486 Busy Here

            - 501 - Not Implemented

            - 505 - Version Not Supported

            - 513 - Message Too Large

            - 603 - Decline

            - 604 - Does Not Exist Anywhere

            - 606 – Not Acceptable

- C3:  Count of INVITES starting a dialog, either sent (e.g. by originating UE) or received depending on measurement point.  Note that retransmitted INVITES should not be counted.

  - For example, if using external protocol sniffer (network probe), then it would have to skip counting retransmissions

  - Call-ID can be used to exclude repeated INVITEs.

    - Description of Call-ID from IETF RFC3261:  Call-ID contains a globally unique identifier for this call, generated by the combination of a random string and the softphone’s host name or IP address.  The combination of the “To” tag, “From” tag, and Call-ID completely defines a peer-to-peer SIP relationship between Alice and Bob and is referred to as a dialog.

- Additional Success Cases mentioned below.

The following cases shall be excluded from setup failures or counted as successful setups (these failure causes maybe not be visible for some measurement points):

          - Call failed due to wrong number, illegal number or incompatible number

          - Call failed due to service provider prohibits providing services

          - The called party is busy and rejects the call, or is busy and does not reject the call

          - The called party is powered off or not in service

          - Call released by peer network (not in service provider’s control) with normal reason

Take 3G VSSR @ MSC as example, the cases above can be measured based on different CS RAB release causes (defined in 3GPP 24.008 10.5.4.11):

| Item | Description | Metrics for 3G VSSR @ MSC |
| --- | --- | --- |
| 1 | Call failed due to wrong number, illegal number or incompatible number | # of CS RAB released with cause code 1: Unassigned (unallocated) number & 22: Number changed & 28: Invalid number format (incomplete number) |
| 2 | Call failed due to service provider prohibits providing services | # of CS RAB released with cause code 8: Operator determined barring |
| 3 | The called party is busy and rejects the call or is busy and did not reject the call | # of CS RAB released with cause code 21 Call Rejected, cause code 17 User busy |
| 4 | The called party is powered off or not in service | # of CS RAB released with cause code 27: Destination out of order |
| 5 | Call released by peer network (not in service provider’s control) with normal reason | No fixed metrics, implementation dependent |

Additional Success Examples for Map Operation Errors

Call barred, cause 21: Call Rejected

Closed user group rejected, cause 29: Facility Rejected

Data missing, cause 38: Network Out of Order

Facility Not Supported, cause 69: Requested Facility Not Implemented

Forwarding Violations, cause 21: Call Rejected

Illegal Mobile Station, cause 21: Call Rejected

- Calculations and Formulas

Measurement is done at the RNC (Radio Network Controller) level (3G), or eNB level (4G) to allow aggregation from Cells, Sites (Node), Clusters, Markets, or nationally.  Additionally, this could be measured by the Network Probe per RNC or eNB.

VSSR (Voice Setup Success Rate) 	= TSSUC / TCATT

= 1 – (TSFAL / TCATT)

Remark:

Both definitions can be used in VSSR calculation, depending on which measurements are available.

#### Table 6.6-1	VSSR Notation

| Identifier | Definition |
| --- | --- |
| E-RABQCI1 | E-UTRAN Radio Access Bearers for QoS Class Identifier (QCI)1 services |
| RABAMR | Radio Access Bearers for Adaptive Multi-Rate (AMR) calls |
| RRCCS | Radio Resource Control for Conversational class Services |
| TCATT | Total Call ATTempts: Total number of attempts calls in the reporting period |
| TSSUC | Total Setup SUCceeded calls: Total number of succeeded calls in the reporting period |

#### Table 6.6-2	VDCR Measurement Identifiers and Formulas

| Identifier | Title | Formula |
| --- | --- | --- |
| VSSR2G | Voice Setup Success Rate – 2G | Will be considered upon request |
| MO VSSR (Option A) @3GUE | Voice Setup Success Rate – 3G UE (Option A) | MO TSSUCOpA@3GUE / TCATTOpA@3GUE |
| TSSUCOpA@3GUE | Total Setup SUCceeded calls in the reporting period - 3G UE (Option A) | Count of calls receipt / sending Layer 3 message ALERTING or CONNECT or CONNECT ACK |
| TCATTOpA@3GUE | Total Call ATTempts calls in the reporting period - 3G UE (Option A) | Count of “AT Dial command” (for test mobiles) or # of CM Service requests sent by UE (for mobile applications) |
| VSSR (Option B) @3GUE | Voice Setup Success Rate – 3G UE(Option B) | TSSUCOpB@3GUE / TCATTOpB@3GUE |
| TSSUCOpB@3GUE | Total Setup SUCceeded calls in the reporting period - 3G UE (Option B) | Count of calls sending “RB Setup Complete” after receiving “RB Setup” with voice service |
| TCATTOpB@3GUE | Total Call ATTempts calls in the reporting period - 3G UE (Option B) | Count of “AT Dial command” (for test mobiles) or # of CM Service requests sent by UE (for mobile applications) |
| VSSR (Option B) @ RNC | Voice Setup Success Rate – 3G RNC | RRCCS SSR * RABAMR SSR |
| RRCCS SSR | RRCCS Setup Success Rate | RRCCS SSR = # of Total Succeeded RRC Connections / # of Total RRC Setup Attempts = # of RRC CONN SETUP COMP / # of RRC CONN REQ Counting rules: Only RRC CONNECTION REQUEST with establishment cause (refer to 3GPP TS25.331 10.3.3.11) “Originating Conversational Call” and “Terminating Conversational Call” and “Emergency Call” to be counted. RRC CONNECTION SETUP COMPLETE will count the successfully established RRC connections, which used the above listed establishment causes in the RRC Connection Request. NOTE: The RRC CONNECTION REQUEST cause in some cases, will not accurately identify a CS call attempt, and the mobiles might use a different cause, e.g. “other” (which can be used for voice or data). The RRC CONN REQ repetition by UE shall not be counted. |
| RABAMR SSR | RABAMR Setup Success Rate | RABAMR SSR = # of Total Succeeded RABAMR assignments / # of Total RABAMR assignmentrequests (note 4*) = (# of RABAMR ASSIGN RESP SETUP SUCCESS + # of RABAMR successfully redirected to other system) / (# of RABAMR SETUP ATTEMPT) Counting rules: Only RAB of AMR all rates for voice service shall be counted. (RAB with “Traffic Class = conversation” and “Source Statistics Descriptor = speech” (refer to 3GPP TS 25.413) shall be counted) # of RABAMR SETUP ATTEMPT does not include the attempts cancelled by the CN. “# of RAB successfully redirected to other system” shall be counted as successful RAB assignment as shown above. (4*) NOTE “# of RABAMR SETUP ATTEMPT” and “# of RABAMR ASSIGN RESP SETUP SUCCESS” is not a sole count of RABAssignmentRequest / RABAssignmentResponse RANAP protocol messages, Alternative counters can be also used. |
| 3G MO VSSR (Option A) @ MSC | MO Voice Setup Success Rate as measured by MSC (3G) (Option A) | MO TSSUC3GOpA @MSC / TCATT3GOpA @MSC |
| MO TSSUC3GOpA @MSC | MO Total Setup SUCceeded calls in the reporting period – MSC (3G) (Option A) | Count of Total ALERTING message or successful RAB Assignment (only for MO call) |
| TCATT3GOpA @MSC | MO Total Call ATTempts calls in the reporting period – MSC (3G) (Option A) | Count of Total CM Service Request with service type “Mobile originating call establishment” and “Emergency call establishment” |
| 3G MO VSSR (Option B) @ MSC | MO Voice Setup Success Rate as measured by MSC (3G) (Option B) | TSSUC3GOpB @MSC / TCATT3GOpB @MSC |
| MO TSSUC3GOpB @MSC | MO Total Setup SUCceeded calls in the reporting period – MSC (3G) (Option B) | Count of Total RAB ASSIGNMENT COMPLETE successful after the optional TMSI reallocation, ciphering and authentication have completed successfully |
| TCATT3GOpB @MSC | MO Total Call ATTempts calls in the reporting period – MSC (3G) (Option B) | Count of SETUP REQUEST from originating user received + SETUP message sent to called user. Subtract those calls that didn’t receive unsupported service/unsubscribed service or timeout of no response to setup message or A party abandon or B party busy or timeout from RAB assignment or TMSI reallocation or encountered radio link failure |
| MO VSSR (Option A) @ Iu-CS | MO Voice Setup Success Rate as measured by the Network Probe @ Iu-CS (3G) (Option A) | MO TSSUC3GOpA@Iu-CS / MO TCATT3GOpA@Iu-CS |
| MO TSSUC3GOpA@Iu-CS | MO Total Setup SUCceeded calls in the reporting period - Network Probe @ Iu-CS (3G) (Option A) | Count of Total Alerting Receptions Counting rules: Only the Alerting Receptions for the originating call shall be counted |
| MO TCATT3GOpA@Iu-CS | MO Total Call ATTempts calls in the reporting period - Network Probe @ Iu-CS (3G) (Option A) | Count of Total MO CM Service Requests Counting rules: Only CM Service Request with Service Type “Mobile originating call establishment” and “Emergency call establishment” shall be counted |
| MO VSSR (Option B) @ Iu-CS | MO Voice Setup Success Rate as measured by the Network Probe @ Iu-CS (3G) (Option B) | TSSUC3GOpB@Iu-CS / TCATT3GOpB@Iu-CS |
| MO TSSUC3GOpB@Iu-CS | MO Total Setup SUCceeded calls in the reporting period - Network Probe @ Iu-CS (3G) (Option B) | Count of RAB assignment complete successful |
| MO TCATT3GOpB@Iu-CS | MO Total Call ATTempts calls in the reporting period - Network Probe @ Iu-CS (3G) (Option B) | Count of RAB setup requests |
| MO VSSR (Option A) @4GUE | Voice Setup Success Rate – 4G UE (Option A) | TSSUCOpA@4GUE / TCATTOpA@4GUE |
| TSSUCOpA@4GUE | Total Setup SUCceeded calls in the reporting period - 4G UE (Option A) | Count of calls receipt / sending SIP INVITE message with response code “180 Ringing” or “SIP 200 OK” or (C1+C2) Counting rules: Only the first INVITE shall be counted to start the session Only the first SIP 180 Ringing in one session shall be counted If 180 Ringing not received, but SIP 200 of same session received, the call setup also succeeded. If both ringing and SIP 200 are received, only the first is counted. |
| TCATTOpA@4GUE | Total Call ATTempts calls in the reporting period - 4G UE (Option A) | Count of “AT Dial command” (for test mobiles) or # of SIP INVITE sent by UE (for mobile applications) or C3 |
| MO VSSR (Option B) @4GUE | Voice Setup Success Rate – 4G UE (Option B) | TSSUCOpB@UE / TCATTOpB@UE |
| TSSUCOpB@4GUE | Total Setup SUCceeded calls in the reporting period - 4G UE (Option B) | Count of calls sending “RRC Connection Reconfiguration Complete” for E-RAB with QCI = 1 (for further study: how to get the type of E-RAB be setup) |
| TCATTOpB@4GUE | Total Call ATTempts calls in the reporting period - 4G UE (Option B) | Count of “AT Dial command” (for test mobiles) or # of SIP INVITE sent by UE (for mobile applications) |
| VSSR (Option B) @ eNB | Voice Setup Success Rate – 4G eNodeB (Option B) | RRC SSR * E-RABQCI1 SSR |
| RRC SSR | RRC Setup Success Rate | RRC SSR = # of Total Succeeded RRC Connections / # of Total RRC Setup Attempts = # of RRC CONN SETUP COMP / # of RRC CONN REQ Counting rules: # of Total Succeeded RRC Connections is pegged when RRC CONN SETUP COMP message is received by eNB. The RRC CONN REQ resend by UE shall not be pegged |
| E-RABQCI1 SSR | E-RABQCI1 Setup Success Rate | E-RABQCI1 SSR = # of Total Succeeded E-RABQCI1 establishments / # of Total E-RABQCI1 establishment attempts = (# of corresponding S1AP INITIAL CONTEXT SETUP RESPONSE containing QCI1 E-RAB + # of corresponding E-RAB SETUP RESPONSE containing QCI1 E-RAB ) / (# of initial ERAB estab requests received from the MME i.e. # of S1AP INITIAL CONTEXT SETUP REQUEST containing QCI1 E-RAB + # of additional E-RAB establishment requests i.e., # E-RABQCI1 SETUP REQUEST is received from MME - # of handover to other eNB during E-RABQCI1 setup (\\if supported\\)) Counting rules: Only INITIAL CONTEXT SETUP REQUEST message / E-RAB SETUP REQUEST message containing QCI = 1 E-RAB and corresponding INITIAL CONTEXT SETUP RESPONSE / E-RAB SETUP RESPONSE shall be counted 3GPP allows HO to interrupt the E-RAB Setup, but the price to pay is to reject the ERAB Setup. For this reason, if this optional procedure is supported (rare) and if a handover becomes necessary during E-RAB Setup, the eNB may interrupt the ongoing E-RAB Setup procedure (refer to 3GPP TS36.413 8.2.1.2). MME will try to setup E-RAB in another eNB (refer to 3GPP TS23.401 5.5.1.1.1). So “# of E-RABQCI1 SETUP REQUEST Interactions with Handover procedure” shall be subtracted from E-RAB establishment attempts as shown in the formula above |
| VSSR4GEMME | Voice Setup Success Rate – 4G MME | MME doesn’t have visibility of voice setup success or failure events, so MME is not a suitable measurement point of VSSR |
| MO VSSR (Option A) @ P-CSCF | MO Voice Setup Success Rate as measured by the P-CSCF (4G) | MO TSSUC4GOpA @P-CSCF / MO TCATT4GOpA @P-CSCF |
| MO TSSUC4GOpA @P-CSCF | Total Setup SUCceeded calls in the reporting period - 4G P-CSCF (Option A) | Count of corresponding SIP 180 Ringing or SIP 200 sent to UE |
| MO TCATT4GOpA @P-CSCF | Total Call ATTempts calls in the reporting period - 4G P-CSCF (Option A) | Count of SIP INVITE received from UE or (C1+C2)/C3 Counting rules: Only the first INVITE shall be counted to start the session Only the first SIP 180 Ringing in one session shall be counted If 180 Ringing not received, but SIP 200 of same session received, the call setup also succeeded. If both ringing and SIP 200 are received, only the first is counted. |
| MO VSSR (Option A) @ Network Probe at S1-U or Mw | Voice Setup Success Rate as measured by 4G Network Probe @ S1-U / Network Probe @ Mw (4G) (Option A) | TSSUC4GOpA @ S1-U or Mw / TSATT4GOpA @ S1-U or Mw Remark: When encryption is applied, SIP message will not be visible to Network Probe @ S1-U. In this case, network probe @ Mw is an alternative option to measure VSSR |
| TSSUC4GOpA @ S1-U or Mw | Total Setup SUCceeded calls in the reporting period - 4G Network Probe @ S1-U / Network Probe @ Mw (4G) (Option A) | Count of corresponding SIP 180 ringing or SIP 200 OK sent to UE |
| TSATT4GOpA @ S1-U or Mw | Total Call ATTempts calls in the reporting period - 4G Network Probe @ S1-U / Network Probe @ Mw (4G) (Option A) | Count of SIP INVITE received from UE or (C1+C2)/C3 Counting rules: Only the first INVITE shall be counted to start the session Only the first SIP 180 Ringing in one session shall be counted If 180 Ringing not received, but SIP 200 of same session received, the call setup also succeeded. If both ringing and SIP 200 are received, only the first is counted. |

- Reported data and format

- Monthly data shall be reported per the frequency and method noted in Sections 3.5.2 and 4.2.2 of the TL 9000 Measurement Handbook

- The VSSR measurement shall be reported for each month and each product category with data elements, or equivalent as defined by the TL 9000 Administrator.

### 6.6.5	Sources of Data

- Service Providers that has access to wireless infrastructure

- Data can be from UE, RNC (3G), eNB (4G), MME (4G), Network Probe @ Iu-CS (3G), Network Probe @ S1-U, or P-CSCF

### 6.6.6	Example of Voice Setup Success Rate as measured by the User Equipment e.g. Test Mobiles or Mobile Application (3G & 4G)

The formula of VSSR measured at UE:

MO VSSR (Option A) @ UE 	= MO TSSUCOpA@UE / TCATTOpA@UE

i)  For 3G

MO TSSUC3GOpA@UE: # of calls receipt / sending Layer 3 message ALERTING or CONNECT or CONNECT ACK

TCATT3GOpA@UE:  # of “AT Dial command” (for test mobiles) or # of CM Service requests sent by UE (for mobile applications)

ii) For 4G

TSSUC4GOpA@UE: # of calls receipt / sending SIP INVITE message with response code “180 Ringing” or “SIP 200 OK”

or (C1+C2)

TCATT4GOpA@UE: # of “AT Dial command” (for test mobiles) or # of SIP INVITE sent by UE (for mobile applications) or C3

Counting rules:

- Only the first INVITE shall be counted to start the session

- Only the first SIP 180 Ringing in one session shall be counted

- If 180 Ringing not received, but SIP 200 of same session received, the call setup also succeeded.  If both ringing and SIP 200 are received, only the first is counted.

VSSR (Option B) @ UE = TSSUCOpB@UE / TCATTOpB@UE

i)  For 3G

TSSUC3GOpB@UE: # of calls sending “RB Setup Complete” after receiving “RB Setup” with voice service

TCATT3GOpB@UE: # of “AT Dial command” (for test mobiles) or # of CM Service requests sent by UE (for mobile applications)

ii)  For 4G

TSSUC4GOpB@UE: # of calls sending “RRC Connection Reconfiguration Complete” for E-RAB with QCI = 1 (for further study: how to get the type of E-RAB be setup)

TCATT4GOpB@UE: # of “AT Dial command” (for test mobiles) or # of SIP INVITE sent by UE (for mobile applications)

### 6.6.7	Example of Voice Setup Success Rate as measured by the RNC (3G)

As shown in Appendix B.1 & B.2, RNC has no visibility on call flows between UE and CN so only Option B is applicable for VSSR @ RNC

In this document, we use voice service radio bearer setup success rate (RRC SSR * RAB SSR) as an estimation of VSSR measured by RNC.

The formula of VSSR measured at RNC (per cell):

VSSR (Option B) @ RNC 		= RRCCS SSR * RABAMR SSR

- RRCCS SSR -- NOTE: only count for a voice call.

RRCCS SSR	= # of Total Succeeded RRC Connections / # of Total RRC Setup Attempts

= # of RRC CONN SETUP COMP / # of RRC CONN REQ

Counting rules:

- Only RRC CONNECTION REQUEST with establishment cause (refer to 3GPP TS25.331 10.3.3.11) “Originating Conversational Call” and “Terminating Conversational Call” and “Emergency Call” to be counted. RRC CONNECTION SETUP COMPLETE will count the successfully established RRC connections, which used the above listed establishment causes in the RRC Connection Request.   NOTE:  The RRC CONNECTION REQUEST cause in some cases, will not accurately identify a CS call attempt, and the mobiles might use a different cause, e.g. “other” (which can be used for voice or data).

- The RRC CONN REQ repetition by UE shall not be counted.

- RABAMR SSR – NOTE: only count for voice calls.

RABAMR SSR	= # of Total Succeeded RABAMR assignments / # of Total RABAMR assignmentrequests (note 4*)

= (# of RABAMR ASSIGN RESP SETUP SUCCESS + # of RABAMR successfully redirected to other system) / (# of RABAMR SETUP ATTEMPT)

Counting rules:

- Only RAB of AMR all rates for voice service shall be counted. (RAB with “Traffic Class = conversation” and “Source Statistics Descriptor = speech” (refer to 3GPP TS 25.413) shall be counted)

- # of RABAMR SETUP ATTEMPT does not include the attempts cancelled by the CN.

- “# of RAB successfully redirected to other system” shall be counted as successful RAB assignment as shown above.

(4*) NOTE “# of RABAMR SETUP ATTEMPT” and “# of RABAMR ASSIGN RESP SETUP SUCCESS” is not a sole count of RABAssignmentRequest / RABAssignmentResponse RANAP protocol messages, Alternative counters can be also used.

### 6.6.8	Example of Voice Setup Success Rate as measured by the MSC (3G)

The optional formulas of VSSR measured by MSC:

3G MO VSSR (Option A) @ MSC	= MO TSSUC3GOpA @MSC / TCATT3GOpA @MSC

= # of Total Alerting receptions / # of Total MO CM service requests

MO TCATT3GOpA @MSC = Total CM Service Request with service type “Mobile originating call establishment” and “Emergency call establishment”.

MO TSSUC 3GOpA @MSC= Total ALERTING message or successful RAB Assignment (only for MO call).

3G VSSR (Option B) @ MSC	= TSSUC3GOpB @MSC / TCATT3GOpB @MSC

= # of RAB assignment complete successful / SETUP sent/received

TSSUC3GOpB @MSC = Total RAB ASSIGNMENT COMPLETE successful after the optional TMSI reallocation, ciphering and authentication have completed successfully.

TCATT3GOpB @MSC= SETUP REQUEST from originating user received + SETUP message sent to called user.  Subtract those calls that didn’t receive unsupported service/unsubscribed service or timeout of no response to setup message or A party abandon or B party busy or timeout from RAB assignment or TMSI reallocation or encountered radio link failure

NOTES:  Option A only applies for MO case. Option B applies to both MO and MT cases.

Counting rules:

- The cases described in 6.6.4 b) shall be counted as successful setup or subtracted from Attempts.

### 6.6.9	Example of Voice Setup Success Rate as measured by the Network Probe @ Iu-CS (3G)

The formula of Mobile Originated VSSR measured by Network Probe @ Iu-CS:

MO VSSR (Option A) @ Iu-CS 	= MO TSSUC3GOpA@Iu-CS / MO TCATT3GOpA@Iu-CS

= # of Total Alerting Receptions / # of Total MO CM Service Requests

VSSR (Option B) @ Iu-CS = TSSUC3GOpB@Iu-CS / TCATT3GOpB@Iu-CS

= # of RAB assignment complete successful / # of RAB setup requests

This assumes that one formula applies to both mobile originating and mobile terminating for Option B.

Counting rules:

- Only CM Service Request with Service Type “Mobile originating call establishment” and “Emergency call establishment”  shall be counted

- Only the Alerting Receptions for the originating call shall be counted

### 6.6.10	Example of Voice Setup Success Rate as measured by the eNB (4G)

eNB has no visibility of call flows between UE and CN, so only Option B is available for VSSR @ eNB.

The formula of VSSR measured by eNB (per cell):

VSSR (Option B) @ eNB 		= RRC SSR * E-RABQCI1 SSR

- RRC  SSR

RRC SSR		= # of Total Succeeded RRC Connections / # of Total RRC Setup Attempts

= # of RRC CONN SETUP COMP / # of RRC CONN REQ

Counting rules:

- # of Total Succeeded RRC Connections is pegged when RRC CONN SETUP COMP message is received by eNB.

- The RRC CONN REQ resend by UE shall not be pegged

- E-RABQCI1 SSR

E-RABQCI1 SSR	= # of Total Succeeded E-RABQCI1 establishments / # of Total E-RABQCI1 establishment attempts

= (# of corresponding S1AP INITIAL CONTEXT SETUP RESPONSE containing QCI1 E-RAB

+

# of corresponding E-RAB SETUP RESPONSE containing QCI1 E-RAB

) /

(# of initial ERAB estab requests received from the MME i.e.

# of S1AP INITIAL CONTEXT SETUP REQUEST containing QCI1 E-RAB

+

# of additional E-RAB establishment requests i.e., # E-RABQCI1  SETUP REQUEST is received from MME

-

# of handover to other eNB during E-RABQCI1  setup (\\if supported\\))

Counting rules:

- Only INITIAL CONTEXT SETUP REQUEST message / E-RAB SETUP REQUEST message containing QCI = 1 E-RAB and corresponding INITIAL CONTEXT SETUP RESPONSE / E-RAB SETUP RESPONSE shall be counted

- 3GPP allows HO to interrupt the E-RAB Setup, but the price to pay is to reject the ERAB Setup. For this reason, if this optional procedure is supported (rare) and if a handover becomes necessary during E-RAB Setup, the eNB may interrupt the ongoing E-RAB Setup procedure (refer to 3GPP TS36.413 8.2.1.2). MME will try to setup E-RAB in another eNB (refer to 3GPP TS23.401 5.5.1.1.1). So “# of E-RABQCI1 SETUP REQUEST Interactions with Handover procedure” shall be subtracted from E-RAB establishment attempts as shown in the formula above.

### 6.6.11	Example of Voice Setup Success Rate as measured by the MME (4G)

MME doesn’t have visibility of voice setup success or failure events, so MME is not a suitable measurement point of VSSR.

### 6.6.12	Example of Voice Setup Success Rate as measured by the P-CSCF (4G)

P-CSCF has no visibility on the radio access bearer setup processes, so only Option A is applicable for VSSR @ P-CSCF.

The formula of VSSR measured by P-CSCF:

MO VSSR (Option A) @ P-CSCF 	= MO TSSUC4GOpA @P-CSCF / MO TCATT4GOpA @P-CSCF

= # of corresponding SIP 180 Ringing or SIP 200 sent to UE / # of SIP INVITE received from UE

or (C1+C2)/C3

Counting rules:

- Only the first INVITE shall be counted to start the session

- Only the first SIP 180 Ringing in one session shall be counted

- If 180 Ringing not received, but SIP 200 of same session received, the call setup also succeeded.  If both ringing and SIP 200 are received, only the first is counted.

### 6.6.13	Example of Voice Setup Success Rate as measured by the Network Probe @ S1-U / Network Probe @ Mw (4G)

At S1-U or Mw, there is no visibility on the radio access bearer setup processes, so only Option A is applicable for VSSR @ S1-U / VSSR @ Mw.

The formula of VSSR measured by Network Probe @ S1-U or Network Probe @ Mw:

MO VSSR (Option A) @ Network Probe at S1-U or Mw

= TSSUC4GOpA @ S1-U or Mw / TSATT4GOpA @ S1-U or Mw

= # of corresponding SIP 180 ringing or SIP 200 OK sent to UE / # of SIP INVITE received from UE

or (C1+C2)/C3

Counting rules:

- Only the first INVITE shall be counted to start the session

- Only the first SIP 180 Ringing in one session shall be counted

- If 180 Ringing not received, but SIP 200 of same session received, the call setup also succeeded.  If both ringing and SIP 200 are received, only the first is counted.

Remark:    When encryption is applied, SIP message will not be visible to Network Probe @ S1-U. In this case, network probe @ Mw is an alternative option to measure VSSR.

Appendix

- 4G VoLTE call flows

A.1 IMS SIP signaling

Remark: Mw interface is the interface between P-CSCF and I/S-CSCF.

A..2 MO VoLTE call flow (with RRC & E-RAB Setup)

A.3 MT VoLTE call flow (with RRC & E-RAB Setup)

Remark:

With precondition enabled, the MT UE will neither alert the user nor reply with 180 Ringing until E-RAB setup is successful.  The call flow would be as shown above.

With precondition disabled, MT UE may alert the user and reply with 180 Ringing before E-RAB setup.

For the details of precondition, please refer to RFC 3312.

- 3G Voice call flows

B.1 MO voice call flow (with RRC & RAB setup)

B.2 MT voice call flow (with RRC & RAB setup)